## Slide 1: 互联网体系结构 拥塞控制

## Slide 2: TCP/IP协议栈
Applications (e.g. Telnet, HTTP)
TCP
UDP
ICMP
ARP
IP
Link Layer (e.g. Ethernet, ATM)
Physical Layer (e.g. Ethernet, SONET)

## Slide 3: 传输层协议
实现端到端的数据传输
  Protocol implemented entirely at the ends
  Fate-sharing
  Completeness/correctness of function implementations
Notes: Fate sharing in unicast applications means that so long as there is a path that IP can find between two applications, then TCP can hang on to the connection as long as they like. However, if either party fails, the connection certainly fails.
Fate-sharing is an engineering design philosophy where related parts of a system are yoked together, so that they either fail together or not at all.

## Slide 4: 传输层协议
UDP provides just integrity and demux
TCP adds…
  Connection-oriented
  Reliable
  Ordered
  Point-to-point
  Byte-stream
  Full duplex
  Flow and congestion controlled

## Slide 5: TCP协议的变迁
1975
1980
1985
1990
1982
TCP & IP
RFC 793 & 791
1974
TCP described by
Vint Cerf and Bob Kahn
In IEEE Trans Comm
1983
BSD Unix 4.2
supports TCP/IP
1984
Nagel’s algorithm
to reduce overhead
of small packets;
predicts congestion collapse
1987
Karn’s algorithm
to better estimate round-trip time
1986
Congestion collapse
observed
1988
Van Jacobson’s algorithms
congestion avoidance and congestion control
(most implemented in 4.3BSD Tahoe)
1990
4.3BSD Reno
fast retransmit
delayed ACK’s
1975
Three-way handshake
Raymond Tomlinson
In SIGCOMM 75
Notes: Nagel’s algorithm. RFC 896: Congestion Control in IP/TCP Internetworks
Karn’s algorithm. TCP adjusts the timeouts in agreement with the Round-Trip-Time (RTT) estimation for the current end-to-end path. RTT estimation is often called Smoothed-Round-Trip-Time (SRTT) and is obtained by averaging the measured RTT for the packets sent so far (the details will be described in the next section). Then, in the original RFC 793 TCP, the retransmit timeout (RTO) is set as twice the SRTT .
A problem arises from the way samples are taken for the calculation of the average: TCP is unable to distinguish two separate acknowledgements for the same sequence number. Therefore, we have the following problem:
A timeout occurs before an ACK is received, and PKT1 is retransmitted. The ack for the first PKT1 arrives a bit later and the source measures a wrong value for the RTT.
Phil Karn, radio-packet enthusiast, proposed the following modification to TCP:
Do not take into account the RTT sampled from packets that have been retransmitted.
On successive retransmissions, set each timeout to twice the previous one.

## Slide 6: TCP协议的变迁
1993
1994
1996
1994
ECN
(Floyd)
Explicit
Congestion
Notification
1993
TCP Vegas
(Brakmo et al)
real congestion avoidance
1994
T/TCP
(Braden)
Transaction
TCP
1996
SACK TCP
(Floyd et al)
Selective Acknowledgement
1996
Hoe
Improving TCP startup
1996
FACK TCP
(Mathis et al)
extension to SACK
2016
2016
BBR
Google
2008
2008
CUBIC
2004
BIC
2004
Notes: RFC1644: T/TCP -- TCP Extensions for Transactions Functional Specification
TCP was designed to around the virtual circuit model, to support streaming of data. Another common mode of communication is a client-server interaction, a request message followed by a response message. The request/response paradigm is used by application-layer protocols that implement transaction processing or remote procedure calls, as well as by a number of network control and management protocols (e.g., DNS and SNMP).
Currently, many Internet user programs that need request/response communication use UDP, and when they require transport protocol functions such as reliable delivery they must effectively build their own private transport protocol at the application layer. Request/response, or "transaction-oriented", communication has the following features:
The fundamental interaction is a request followed by a response.
(b) An explicit open or close phase may impose excessive overhead.
(c) At-most-once semantics is required; that is, a transaction must not be "replayed" as the result of a duplicate request packet.
(d) The minimum transaction latency for a client should be RTT + SPT, where RTT is the round-trip time and SPT is the server processing time.
(e) In favorable circumstances, a reliable request/response handshake should be achievable with exactly one packet in each direction.
Hoe. Improving the Start-up Behavior of a Congestion Control Scheme for TCP. Sigcomm 1996.

## Slide 7: 可靠性模型
Reliability => requires redundancy to recover from uncertain loss or other failure modes
Two types of redundancy:
  Spatial redundancy independent backup copies
    Forward error correction (FEC) codes
    Problem: requires huge overhead, since the FEC is also part of the packet(s) it cannot recover from erasure of all packets
  Temporal redundancy retransmit if packets lost/error
    Lazy: trades off response time for reliability
    Design of status reports and retransmission optimization important

## Slide 8: 前向纠错编码
add redundancy to recover from losses
original file (n blocks)
infinite number of blocks
encoding
lossy channel
receive (1+e) blocks
recover file
decoding

## Slide 9: 时序冗余模型
Packets
Sequence Numbers
CRC or Checksum
Status Reports
ACKs
NAKs
SACKs
Bitmaps
Retransmissions
Timeout

## Slide 10: 错误的类型和效果
Forward channel bit-errors (garbled packets)
Forward channel packet-errors (lost packets)
Reverse channel bit-errors (garbled status reports)
Reverse channel packet-errors (lost status reports)
Protocol-induced effects:
  Duplicate packets
  Duplicate status reports
  Out-of-order packets
  Out-of-order status reports
  Out-of-range packets/status reports (in window-based transmissions)

## Slide 11: 基本机制
Mechanisms:
  Checksum in pkts: detects pkt corruption
  ACK: “packet correctly received”
  NAK: “packet incorrectly received”
Provides reliable transmission over:
  A forward channel which has bit-errors; reverse: ok
Cannot handle reverse-channel bit-errors; or packet-losses in either direction

## Slide 12: 更多的机制
Mechanisms:
  Checksum: detects corruption in pkts & acks
  ACK: “packet correctly received”
  NAK: “packet incorrectly received”
  Sequence number: 1-bit sequence number used
Provides reliable transmission over:
  A forward & reverse channel with bit-errors
  Detects duplicates of packets/acks/naks
Still needs NAKs, and cannot recover from packet errors

## Slide 13: 更多的机制
Mechanisms:
  Checksum: detects corruption in pkts & acks
  ACK: “packet correctly received”
  Duplicate ACK: “packet incorrectly received”
  Sequence number
Provides reliable transmission over:
  A forward & reverse channel with bit-errors
  Detects duplicates of packets/acks
  NAKs eliminated
Packet errors in either direction not handled

## Slide 14: 可靠性机制
Mechanisms:
  Checksum: detects corruption in pkts & acks
  ACK: “packet correctly received”
  Duplicate ACK: “packet incorrectly received”
  Sequence number
  Timeout only at sender
Provides reliable transmission over:
  A forward & reverse channel with bit-errors
  Detects duplicates of packets/acks
  NAKs eliminated
  A forward & reverse channel with packet-errors (loss)

## Slide 15: Best Effort
The Internet Protocol (IP) w/o TCP
  the network simply does its best to deliver your data as efficiently as possible.
  There are no guarantees
Problem
  they might reach the other end very quickly,
  they might reach somewhat slower
  or they might never even make it.

## Slide 16: The Success of Internet
IP has no guarantees
  Link failure (hence routes are recalculated)
  Congestion
  …
TCP
  Provide e2e reliable transfer with congestion control
  That’s why Internet protocol stack is referred to as TCP/IP

## Slide 17: Congestion
Congestion occurs when resource demands exceed the capacity.
As users come and go, so do the packets they send;
Internet performance is therefore largely governed by these inevitable natural fluctuations.

## Slide 18: Definition
There is no ‘official’, universally accepted definition of network congestion
An elaborate attempt
  A network is said to be congested from the perspective of a user if the service quality noticed by the user decreases because of an increase in network load.
    [ Keshav S (1991) Congestion Control in Computer Networks PhD thesis UC Berkeley.]

## Slide 19: 拥塞：公共资源的悲剧
Hardin Science 1968
Different sources compete for “common” or “shared” resources inside network
  Sources are unaware of current state of resource
  Sources are unaware of each other
  Conflicts with collective interests: if all sources do this to drive the system to overload, throughput gain is NEGATIVE, and worsens rapidly with incremental overload => congestion collapse!!
The Tragedy of the Commons
Notes: Hardin于1968年发表于Science的文章“公用的悲剧”(The Tragedy of the Commons)可以说是迄今为止描述资源两难问题的最有影响力的文章。在文中Hardin认为现代人过度使用资源的后果将是面临类似于使用同一牧场的牧人所面临的悲剧：在公用牧场之中放牧的牧人尽可能地多饲养牲口以使自己的利益最大化，而这种行为导致的长期后果是牲口的总数超出了牧场所能容纳的极限，草资源很快枯竭。所有的牲口也因为没有足够的食物而面临饿死的境地。
引入产权是此问题的主要解决方案。

## Slide 20: 拥塞：公共资源的悲剧
In October 1986 the ARPANET suffered major congestion collapse
The effects of this collapse were later described by Van Jacobson
  Data throughput from LBL to UC Berkeley (sites separated by 400 yards and two IMP hops) dropped from 32 Kbps to 40bps
Notes: Hardin于1968年发表于Science的文章“公用的悲剧”(The Tragedy of the Commons)可以说是迄今为止描述资源两难问题的最有影响力的文章。在文中Hardin认为现代人过度使用资源的后果将是面临类似于使用同一牧场的牧 人所面临的悲剧：在公用牧场之中放牧的牧人尽可能地多饲养牲口以使自己的利益最大化，而这种行为导致的长期后果是牲口的总数超出了牧场所能容纳的极限，草资源很快枯竭。所有的牲口也因为没有足够的食物而面临饿死的境地。

## Slide 21: Van Jacobson
Jacobson is best known for his work in redesigning TCP/IP's flow control algorithms (Jacobson's algorithm) is said to have saved the Internet
Furthermore he has co-written a few widely used tools, such as traceroute, pathchar and tcpdump
For his work, Jacobson received the 2001 ACM SIGCOMM Award

## Slide 22: Congestion Control
Two sides of the same coin
  pre-allocate resources so at to avoid congestion
  control congestion if (and when) is occurs

## Slide 23: Example
Consider an ISP that would allow up to 1000 simultaneous data flows
Each of which would have a maximum rate of 1 Mbps, but an average rate of only 300 kbps.
Would it make sense to connect their Internet gateway to a 1 Gbps link (which means that all of them could be accommodated at all times), or would, say, 600 Mbps be enough?

## Slide 24: Example (Cont’d)
assume that the ISP chooses the 600 Mbps option (since it’s cheaper)
In this case, the gateway would see occasional traffic spikes that go beyond the capacity limit if a certain number of customers use their maximum rate at the same time.

## Slide 25: Consequence
Since these excess packets cannot be transferred across the link
there are only two things that this device can do:
  buffer the packets (however queue is limited)
  or drop them.
When queues grow, the network is said to be congested; this effect will manifest itself in increasing delay and, at worst, packet loss.

## Slide 26: Overprovision or control?
Overprovision
  the common choice of ISPs is to serve the aforementioned 1000 flows with 1 Gbps or even more in order to avoid congestion within their network.
Congestion control
  The goal of congestion control mechanisms is simply to use the network as efficiently as possible,
  attain the highest possible throughput while maintaining a low loss ratio and small delay.

## Slide 27: Congestion Control
From overprovision to control
‘how to eliminate congestion’
‘how to efficiently use all the available capacity’.

## Slide 28: Congestion Collapse
The Internet first experienced a problem called congestion collapse in the 1980s.
Referred to as when a condition occurs where increasing sender rates reduces the total throughput of a network.
it is described as a stable condition of degraded performance that stems from unnecessary packet retransmissions.

## Slide 29: Example 1
1
2
3
4
5
0
100kbps
100kbps
300kbps
1Mbps
100kbps
Link capacity
0-2,1-2,3-4:100kbps
2-3:300kbps
3-5:1Mbps
Two UDP connections: 04, 15
Each source started with a rate of 64 kbps and increased it by 3 kbps every second. (no decease phase)

## Slide 30
In Example 1, there will be no collapse
throughput increases until both senders reach the capacity limit of their access links. There is no collapse
1
2
3
4
5
0
100kbps
100kbps
300kbps
1Mbps
100kbps

## Slide 31: Example 2
but what happens when the bandwidth of the 0–2 (100k1M) link is increased?
1
2
3
4
5
0
1Mbps
100kbps
300kbps
1Mbps
100kbps

## Slide 32: Congestion Collapse
For 15: as the rate approaches the capacity limit, the throughput curve becomes smoother (knee), beyond a certain point, it suddenly drops (the so-called cliff) and then decreases further.
While 04 remains almost same, (limited to 100 kbps by the connection between nodes 3 and 4.)
1
2
3
4
5
0
1Mbps
100kbps
300kbps
1Mbps
100kbps

## Slide 33: Strange Phenomenon
Congestion at node 2 – a queue will grow
Roughly, for every packet from customer 1, there are 10 packets from customer 0.
Basically, this means that the packets from customer 0 unnecessarily occupy bandwidth of the bottleneck link that could be used by the data flow coming from customer 1
the rate will be narrowed down to 100 kbps at the 3–4 link anyway.
The more the customer 0 sends, the greater this problem.

## Slide 34: Queue at Router 2
since both sources keep increasing their rates no matter what the capacities beyond their access links are, there will be congestion at node 2 – a queue will grow,
and this queue will have more packets that stem from customer 0.

## Slide 35: 拥塞过程的全貌
knee – point after which
  throughput increases very slowly
  delay increases fast
cliff – point after which
  throughput starts to decrease very fast to zero (congestion collapse)
  delay approaches infinity
Note (in an M/M/1 queue)
  delay = μ-1/(1 – ρ)
  ρ= λ/ μ
Load
Load
Throughput
Delay
knee
cliff
congestion
collapse
packet
loss
Notes: ρ= λ/ μ
λ是到达速率
μ是服务速率

## Slide 36: The Need for Congestion Control
If customer 0 knew that it would never attain more throughput than 100 kbps and would therefore refrain from increasing the rate beyond this point, customer 1 could stay at its limit of 100 kbps.
A technical solution is required for appropriately reducing the rate of customer 0; this is what congestion control is all about.

## Slide 37: Why Congestion Control
1. Avoid congestion collapse (for the whole network)
2. Fairness (for other opponent flows)
3. Better achieve its own goals in delay/loss/throughput (for applications)

## Slide 38: Congestion Avoidance
Schemes that allow the network to operate at the knee are called congestion avoidance schemes, whereas congestion control just tries to keep the network to the left of the cliff.
In practice, it is hard to differentiate mechanisms like this as they all share the common goal of maximizing network throughput while keeping queues short.
Sometime interchangeable

## Slide 39: 拥塞控制和拥塞避免
Congestion control goal
  stay left of cliff
Congestion avoidance goal
  stay left of knee
Right of cliff:
  Congestion collapse
Load
Throughput
knee
cliff
congestion
collapse

## Slide 40: 拥塞控制和拥塞避免
唐代孙思邈《千金要方·论诊候第四》
古人善为医者，上医医未病之病，中医医欲病之病，下医医已病之病，若不加心用意，於事混淆，即病者难以救矣
扁鹊曰：长兄于病视神，未有形而除之，故名不出于家。中兄治病，其在毫毛，故名不出于闾。若扁鹊者，血脉、投毒药、副肌肤间，而名出闻于诸侯 《鹖冠子》

## Slide 41: 拥塞崩溃
Definition: Increase in network load results in decrease of useful work done
Many possible causes
  Spurious retransmissions of packets still in flight
  Undelivered packets
    Packets consume resources and are dropped elsewhere in network
  Fragments
    Mismatch of transmission and retransmission units
  Control traffic
    Large percentage of traffic is for control
  Stale or unwanted packets
    Packets that are delayed on long queues

## Slide 42: Congestion control and flow control
The goal of flow control is to protect the receiver from overload, whereas the goal of congestion control is to protect the network.
The two functions lend themselves to combined implementations because the underlying mechanism is similar:
  feedback is used to tune the rate of a flow.
  Sending rate= MIN (flow controled, congestion controled)
Sometimes also interchangeable, or one is regarded as a special case of the other

## Slide 43: Example
15: max rate=100kbps by CC
However, if 5 can only process data (e.g. read buffer) at 50kbps, then flow control enforced

## Slide 44: Congestion Control History
Congestion control is a very old research topic. (about 30 years)
  In Oct. 1986, 5,089 hosts on Internet
  Internet suffered from it’s first collapse
Reason
  Early TCP (from 1974) flow control only prevents overwhelming receivers
  Paths clogged with unnecessarily-retransmitted packets

## Slide 45: Milestone in Congestion Control
Milestone: Van Jacobson,” Congestion Avoidance and Control”, ACM SIGCOMM 1988
  TCP Tahoe (include congestion control in TCP)

## Slide 46: Congestion Control Today
Now, it’s still a hot topic
  In specific networks (wireless, data center)
  In specific scenarios (LFP…)
  with new methods (e.g. machine learning)

## Slide 47: ACM SIGCOMM 2014

## Slide 48: ACM SIGCOMM 2015

## Slide 49: ACM SIGCOMM 2016

## Slide 50: ACM SIGCOMM 2017

## Slide 51: ACM SIGCOMM 2018

## Slide 52: ACM SIGCOMM 2019

## Slide 53: ACM SIGCOMM 2020

## Slide 54: Trends in Congestion Control
Trend #1: New datapaths
Apps with strict perf reqs
Apps with unique needs

## Slide 55: Trend #2: New algorithms
1987
2018
Vegas
Westwood
Compound
PRR
BIC
H-TCP
Cubic
FAST
EBCC
Binomial
LEDBAT
Veno
BBR
PCC
Remy
Sprout
DCTCP
Illinois
NV
Hybla
TIMELY
ABC
NewReno
Copa
RC3
XCP
RCP
DCQCN
1998
2001
Tahoe
Reno
2010
Vivace
Indigo
Nimbus
Improving deployed algorithms
Changing application requirements
Different deployment scenarios
Using new algorithmic tools

## Slide 56
There are many new challenges for Congestion control
but we need understand the basic Design Considerations first

## Slide 57: CC: Design Considerations
How could one design a mechanism that automatically and ideally tunes the rate of the flow from customer 0 in our example?
A typical solution:
  measure the network state
  control the rate
But, how?

## Slide 58: 3 elements
3 elements involved in connection:
  Traffic originates from a sender
  each packet usually traverses a certain number of intermediate nodes
  traffic reaches a receiver.
2
3
1
5

## Slide 59: CC: Design Considerations
Controllers
  Traffic can be controlled at the sender and at the intermediate nodes;
Measuring points
  performance measurements can be taken by intermediate nodes and by the receiver.
at least one controller and one measuring point must participate in any congestion control scheme that involves feedback.

## Slide 60: Closed-loop versus open-loop
In control theoretic terms, systems that use feedback are called closed-loop control as opposed to open-loop control systems, which have no feedback.
Neglecting feedback is clearly not a good choice when it comes to dissolving network congestion
  dynamics of the system – the presence or absence of other flows

## Slide 61: Open-loop case
applying open-loop control would mean using a priori knowledge about the network
  for example, the bottleneck bandwidth
  If the access link is the bottleneck, the sender thus can limit its sending rate without feedback

## Slide 62: Feedback
a general-purpose congestion control scheme will normally have the sender tune its rate on the basis of feedback from the receiver
Recall that
  Measuring points: intermediate nodes /receiver.
  However adding measuring functions within network will complicate things significantly
implicit feedback
  measurements that are taken at the receiver and can be used to deduce what happens within the network.

## Slide 63: Implicit Feedback
What can happen to a packet as it travels from source to destination? from an end-node perspective,
  1. It can be delayed.
  2. It can be dropped.
  3. It can be changed.

## Slide 64: Delay
Delay can have several reasons:
  Distance :sending a signal to a satellite and back again takes longer than sending it across an undersea cable
  queuing processing in the involved nodes
  or retransmissions at the link layer.

## Slide 65: Packet Drop
a queue length is exceeded,
a user is not admitted,
equipment malfunctions,
link noise causes a checksum of relevance to intermediate systems to fail. (e.g. packet will be discarded upon checksum mismatch at router)

## Slide 66: Changing a packet
altering its header or its content (payload).
How do we choose a feedback?
  …

## Slide 67: Queue
Good news: ‘queue’ was mentioned twice
  Delay and drop
  at least the factors ‘delay’ and ‘packet dropped’ can indicate congestion.
Bad news:
  Each can happen to a packet can have quite a variety of reasons
Relying on these factors therefore means that implicit assumptions are made about the network
  e.g. assuming that increased delay always indicates queue growth could mean that it is assumed that a series of packets will be routed along the same path).

## Slide 68: Packet loss
Packet loss can be regarded as an the implicit feedback
What the problem?
  Provided that packets are mainly dropped when queues overflow;
  For wireless
    wireless (and therefore noisy) Internet connections poses a problem because it leads to a misinterpretation of packet loss;

## Slide 69: Binary feedback
let us once again focus on the simplest case:
  a notification that tells the source ‘there was congestion’.
What can a sender do in response to a notification that simply informs it that the network is congested?
  Obviously, in order to avoid congestion collapse, it should reduce its rate.
If there was no congestion
  Need a rule for the sender that says ‘increase the rate if the receiver says that there was no congestion

## Slide 70: 拥塞控制的解决思路
End-to-end congestion control
no explicit feedback from network
congestion inferred from end-system observed loss, delay
approach taken by TCP
Network can help
routers provide feedback to end systems
  single bit indicating congestion (SNA, DECbit, TCP/IP ECN, ATM)
  explicit rate sender should send at

## Slide 71: 端到端模型
End-systems is ultimately the source of “demand”
End-system must robustly estimate the timing and degree of congestion and reduce its demand appropriately
Must trust other end hosts to do right thing
End-systems can be helped to detect congestion by routers
Key: trust and complexity resides at end-systems
Issue: What about misbehaving flows?

## Slide 72: 基本控制模型
Let’s assume window-based operation
Reduce window when congestion is perceived
  How is congestion signaled?
    Either mark or drop packets
  When is a router congested?
    Drop tail queues – when queue is full
    Average queue length – at some threshold
Increase window otherwise
  Probe for available bandwidth – how?

## Slide 73: 如何检测拥塞
Explicit network signal
  Send packet back to source (e.g. ICMP Source Quench)
    Control traffic congestion collapse
  Set bit in header (e.g. DEC DNA/OSI Layer 4, ECN)
    Can be subverted by selfish receiver
  Unless on every router, still need end-to-end signal
  Could be robust, if deployed

## Slide 74: 如何检测拥塞
Implicit network signal
  Loss (e.g. TCP Tahoe, Reno, New Reno, SACK)
    +relatively robust, -no avoidance
  Delay (e.g. TCP Vegas, BBR)
    +avoidance, -difficult to make robust
  Easily deployable
  Robust enough? Wireless?