## Slide 1: Programmable Data Plane 可编程数据平面 Internet Architecture

## Slide 2: 控制平面/数据平面
Control plane: Establishing routes for end-to-end connectivity, longer timescales of a few ms
  路由软件，实现路径计算
Data plane: packet-to-packet behavior of a switch, short timescales of a few ns
  可编程交换机等网络设备，实现数据包的处理功能

## Slide 3: 回顾SDN
With the introduction of the Software-defined Networking (SDN) paradigm, control plane has emerged as a separate entity, a logically centralized controller,
  with some of the device control plane functions separated out and moved to this network-level functionality.
the individual switches do not need to implement the logic required to maintain packet forwarding policies locally (e.g., they do not run routing protocols to build routing tables);
  rather, they get these policies prefabricated from the network control plane.
  Here, the controller-switch communication occurs through a standardized southbound API, e.g. OpenFlow

## Slide 4: 控制平面可编程
SDN主要关注控制平面/数据平面分离，在控制平面提供编程性
  It distinguishes SDN from traditional networks
  Source of many (perceived) challenges and opportunities
What about the data plane?
  Which features should be provided in the data plane?
灵活添加新功能!
4
控制器
交换机

## Slide 5: 数据平面提供哪些功能？
基本功能 Streaming algorithms that act on packets
  Matching on some bits, taking a simple action
  … at behest of control and management plane
多样性
  Forwarding
  Access control
  Mapping header fields
  Traffic monitoring
  Buffering and marking
  Shaping and scheduling
  Deep packet inspection

## Slide 6: 特点1: 高速 A Need for Speed
High link speed
  10 Gbps, 40 Gbps, 100 Gbps
Small packets
  40-byte TCP ACK packets
Small time per packet
  40 Gbps =124 Mpps with 320-bit packets
  8 ns to process a packet
Routers need low latency
  Relatively limited opportunity to batch or pipeline

## Slide 7: 特点2: 异构 A Range of Technologies
ASIC (App-Specific Integrated Circuit)
  Fast, dense chip, but expensive to change
FPGAs and network processors
  Fast, reconfigurable, hard to program
Graphics Processing Units
  Massive parallel computation on small cores
Software on commodity computer
  Easy to program, but I/O bandwidth, memory copying, and interrupt overheads

## Slide 8: Packet Forwarding

## Slide 9: Packet Forwarding
Control plane computes a forwarding table
  Maps destination address(es) to an output link
Handling an incoming packet
  Match: destination address
  Action: direct the packet to the chosen output link
Switching fabric
  Directs packet from input link to output link
Switching
Fabric
Processor

## Slide 10: Switch: Match on Destination MAC
MAC addresses are location independent
  Assigned by the vendor of the interface card
  Cannot be aggregated across hosts in the LAN
mac1 | 
mac2 | 
mac3 | 
mac4 | 
mac5 | 
host
host
host
...
mac1
mac2
mac3
switch
host
host
mac4
mac5
Implemented using a hash table or a content addressable memory.

## Slide 11: IP Routers: Match on IP Prefix
IP addresses grouped into common subnets
  Allocated by ICANN, regional registries, ISPs, and within individual organizations
  Variable-length prefix identified by a mask length
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table
Prefixes may be nested. Routers identify the longest matching prefix.

## Slide 12: Switch Fabric: From Input to Output
Lookup
Address
Update
Header
Header Processing
Address
Table
Lookup
Address
Update
Header
Header Processing
Address
Table
Lookup
Address
Update
Header
Header Processing
Address
Table
Queue
Packet
Buffer
Memory
Queue
Packet
Buffer
Memory
Queue
Packet
Buffer
Memory
Data
Hdr
Data
Hdr
Data
Hdr
1
2
N
1
2
N

## Slide 13: Access Control

## Slide 14: Access Control: Packet Filtering
“Five tuple” for access control lists (ACLs)
  Source and destination IP addresses
  TCP/UDP source and destination ports
  Protocol (e.g., UDP vs. TCP)
Can be more sophisticated
  E.g., block all TCP SYN packets from outside hosts
Should arriving packet be allowed in? Departing packet let out?

## Slide 15: Applying Access Control Lists
Ordered list of “accept/deny” clauses
  A clause can have wild cards
  Clauses can overlap
  … so order matters
Packet classification
  Given all of the fields
  … identify the match with the highest priority
Two approaches
  Clever algorithms for multi-dimensional classification
  Ternary Content Addressable Memories (TCAMs)
Src=1.2.3.4, Dest=5.6.7.8 | Deny
Dest=1.2.3.* | Allow
Dest=1.2.3.8, Dport!=53 | Deny
Src=1.2.3.7, Dport=100 | Allow
Dport=100 | Deny

## Slide 16: Mapping Header Fields

## Slide 17: Network Address Translation (NAT)
NAT
inside
outside
10.0.0.1
10.0.0.2
138.76.29.7

## Slide 18: Mapping Addresses and Ports
Remap IP addresses and TCP/UDP port numbers
  Addresses: between end-host and NAT addresses
  Port numbers: to ensure each connection is unique
Create table entries as packets arrive
  Src 10.0.0.1, Sport 1024, Dest 1.2.3.4, Dport 80
    Map to Src 138.76.29.7, Sport 1024, Dest 1.2.3.4, Dport 80
  Src 10.0.0.2, Sport 1024, Dest 1.2.3.4, Dport 80
    Map to Src 138.76.29.7, Sport 1025, Dest 1.2.3.4, Dport 80
Challenges
  When to remove the entries
  Running services behind a NAT
  What if both ends of a connection are behind NATs

## Slide 19: Traffic Monitoring

## Slide 20: Observing Traffic Passing Through
Applications of traffic measurement
  Usage-based billing
  Network engineering
  Detecting anomalous traffic
input
output
source AS
source
prefix
source
dest AS
dest
prefix
dest
intermediate AS

## Slide 21: Passive Traffic Monitoring
Counting the traffic
  Match based on fields in the packet header
  … and update a counter of #bytes and #packets
Examples
  Link
  IP prefixes
  TCP/UDP ports
  Individual “flows”
Challenges
  Identify traffic aggregates in advance vs. reactively
  Summarizing other information (e.g., time, TCP flags)
  Not knowing if you see all packets in a connection
Dest Prefix | #Packets | #Bytes
1.2.3.0/24 | 3 | 1500
7.8.0.0/16 | 10 | 13000
8.0.0.0/8 | 100 | 85020
7.7.6.0/23 | 1 | 40

## Slide 22: More on the motivation for Traffic Monitoring
Needs of Service Providers
  Understand the behavior of their networks
  Provide fast, high-quality, reliable service to satisfy customers and thus reduce churn rate
  Plan for network deployment and expansion
  SLA monitoring, Network security
  Increase Revenue!
    Usage-based billing for network users (like telephone calls)
    Marketing using CRM data
Needs of Customers
  Want to get their money’s worth
  Fast, reliable, high-quality, secure, virus-free Internet access
To Satisfy Service Providers’ Needs to Satisfy Their Customers!

## Slide 23: Motivation (2/2)
Application Areas
  Network Problem Determination and Analysis
  Traffic Report Generation
  Intrusion & Hacking Attack (e.g., DoS, DDoS) Detection
  Service Level Monitoring (SLM)
  Network Planning
  Usage-based Billing
  Customer Relationship Management (CRM)
  Marketing

## Slide 24: Problems
Capturing Packets
  High-speed networks (Mbps  Gbps  Tbps)
  High-volume traffic
  Streaming media (Windows Media, Real Media, Quicktime)
  P2P traffic
  Network Security Attacks
Flow Generation & Storage
  What packet information to save to perform various analysis?
  How to minimize storage requirements?
Analysis
  How to analyze and generate data needed quickly?
  What kinds of info needs to be generated?  Depends on applications

## Slide 25: Research & Development Goals
Develop Methods to
  Capture all packets
  Generate flows
  Store flows efficiently
  Analyze data efficiently
  Generate various reports or information that are suitable for various application areas
Develop a Flexible, Scalable Traffic Monitoring and Analysis System for
  High-speed
  High-volume
  Rich media IP networks

## Slide 26: Network Monitoring Metrics (1/5)
One way loss
RT loss
One way delay
RT delay
Capacity
Bandwidth
Throughput
Delay variance
Network Monitoring
Metrics
Availability
Connectivity
Functionality
Loss
Delay
Utilization

## Slide 27: Network Monitoring Metrics (2/5)
Availability
  The percentage of a specified time interval during which the system was available for normal use
  What is supposed to be available?
    Service, Host, Network
  Availabilities are usually reported as a single monthly figure
    99.99% availability means that the service is unavailable for 4 minutes during a month
  One can test availability by sending suitable packets and observing the answering packets (latency, packet loss)
  Metrics
    Connectivity: the physical connectivity of network elements
    Functionality: whether the associated system works well or not

## Slide 28: Network Monitoring Metrics (3/5)
Packet Loss
  The fraction of packets lost in transit from a host to another during a specified time interval
  Internet packet transport works on a best-effort basis, i.e., a router may drop them depending on its current conditions
  A moderate level of packet loss is not in itself tolerable
    Some real-time services, e.g., VoIP, can tolerate some packet losses
    TCP resends lost packets at a slower rate
  Metrics
    One way loss
    Round Trip (RT) loss

## Slide 29: Network Monitoring Metrics (4/5)
Delay (Latency)
  The time taken for a packet to travel from a host to another
  Round Trip Time (RTT)
    Forward transport delay + server delay + backward transport delay
  Forward transport delay is often not the same as backward transport delay (may use different paths)
  For streaming applications, high delay or delay variation (jitter) can cause degradation on user-perceived QoS
  Metrics
    One way delay
    Round Trip Time (delay)
    Delay variance (jitter)

## Slide 30: Network Monitoring Metrics (5/5)
Throughput
  The rate at which data is sent through the network, usually expressed in bytes/sec, packets/sec, or flows/sec
  Be careful in choosing the interval; a long interval will average out short-term bursts in the data rate
    A good compromise is to use one- to five-minute intervals, and to produce daily, weekly, monthly, and yearly plots
  Link Utilization over a specified interval is simply the throughput for the link expressed as a percentage of the access rate
  Metrics
    Link Capacity (Mbps, Gbps)
    Throughput (bytes/sec, packets/sec, flows/sec)
    Utilization (%)

## Slide 31: Traffic Monitoring Approaches (1/4)
Active Monitoring
Passive Monitoring

## Slide 32: Traffic Monitoring Approaches (2/4)
Active Monitoring
  Performed by sending test (probe) traffic into network
    Generate test packets periodically or on-demand
    Measure performance of test packets or responses
    Take the statistics
  Impose extra traffic on network and distort its behavior in the process
  Test packet can be blocked by firewall or processed at low priority by routers
  Mainly used to monitor network performance
Test packet
generator
Test packet
probe
Response
Probe
Target
host

## Slide 33: Traffic Monitoring Approaches (3/4)
Passive Monitoring
  Carried out by observing network traffic
    Collect packets from a link or network flow from a router
    Perform analysis on captured packets for various purposes
  Network device performance degrades by mirroring or flow export
  Used to perform various traffic usage/characterization analysis or intrusion detection
Flow
Data
Traffic
Information
Packet
Capture
Traffic
Analysis
Flow
Generation
Network link
Router

## Slide 34: Traffic Monitoring Approaches (3/4)
Comparison of Two Monitoring Approaches
 | Active Monitoring | Passive Monitoring
Configuration | Multi-point | Single or multi-point
Data size | Small | Large
Network overhead | Additional traffic | Device overhead No overhead if splitter is used
Purpose | Delay, packet loss, availability | Throughput, traffic pattern, trend, & detection
CPU Requirement | Low to Moderate | High
Advantages | Gain some benefits at the initial stage of network construction, because not much data gained from passive one | Measured result may show the real network characteristics Does not need to generate additional probe messages
Disadvantages | Cannot reflect network characteristics Need to generate the probe messages which may cause extra overhead to network | Captured data has massive volume size Should have additional facility to capture the mirrored packet from network

## Slide 35: Active Monitoring Techniques
ICMP-based Method
  Diagnose network problems
  Availability / Round-trip delay / Round-trip packet loss
TCP-based Method
  One-way bandwidth / Round trip bandwidth
  Bulk transfer rate
UDP-based Method
  One-way packet loss / Round trip bandwidth

## Slide 36: Passive Monitoring Techniques
Packet Capturing
  Packets can be captured using Port Mirroring or Network Splitter (Tap)
Mirroring
Probe system
Splitting
Probe system
 | Port Mirroring | Network Splitter
How it works | - Copies all packets passing on a port to another port | - Splits the signal and sends a signal to original path and another to probe
Advantage | - No extra hardware required | - No processing overhead on router/switch
Disadvantage | - Processing overhead on router/switch | - Splitter hardware required

## Slide 37: Packet Capturing (2/2)
Difficulties in packet capturing
  Massive amount of data
    How much packet data is generated from 100 Mbps network in an hour?
     Port speed ⅹIn&Out ⅹLink Utilization ⅹ sec/hour = throughput
    100 Mbps ⅹ 2 ⅹ 0.5 ⅹ 3600 = 360 Gbps
     Throughput / avg. packet lengthⅹ bytes of packet data = data size
    360 Gbps / (1500 ⅹ 8) ⅹ 30 = 1 Gbyte
  Processing of high-speed packets
    Processing time for 100 Mbps network
    Port speed ⅹ In&Out ⅹ Link Utilization / average packet length
    = 8333 packets/sec => 0.12 msec/packet
 | 100 Mbps | 1 Gbps | 1 Tbps
Data size per hour (assume 0.5 link util) | 1 Gbyte | 10 Gbyte | 10 Tbyte
Processing Time per packet | 0.12 msec | 0.012 msec | 0.012 μsec

## Slide 38: Sampling
Why We Need Sampling?
  If the rate is too high to capture all packets reliably, there is no alternative but to sample the packets
  Sampling algorithms: every Nth packet or fixed time interval
1 2 3 4 5 6 7 8 9 10 11
(a) 2:1 sampling
(b) 1 msec sampling
0 msec
1 msec
2 msec
3 msec
4 msec

## Slide 39: Flow Generation
Flow
  Flow is a collection of packets with the same {SRC and DST IP address, SRC and DST port number, protocol number}
  Flow data can be collected from routers directly, or standalone flow generator having packet capturing capability
  Popular flow formats
    NetFlow (Cisco), sFlow (sFlow.org), IPFIX (IETF)
  Issues in flow generation
    What information should be included in a flow data?
    How to generate flow data from raw packet information efficiently?
    How to save bulk flow data into DB or binary file in a collector?
    How long should the data be preserved?
flow 4
flow 1
flow 2
flow 3

## Slide 40: Traffic Analysis Aspects
Spatial Aspect
  The patterns of traffic flow relative to the network topology
  Important for proper network design and planning
  Identification of bottleneck & avoidance of congestion
  Example: Flow aggregation by src, dst IP address or AS number
Temporal Aspect
  The stochastic behavior of a traffic flow, described in statistical terms
  Important for resource management and traffic control
  Important for traffic shaping and caching policies
  Example: Packet or byte per hour, day, week, month
Composition of Traffic
  A breakdown of traffic according to the contents, application, packet length, flow duration
  Helps to explain its temporal and spatial characteristics
  Example: game, streaming media traffic for a week from peer ISP

## Slide 41: Traffic Classification/Identification (1/2)
Traffic Classification
  Classifying traffic based on features passively observed in the traffic, and according to specific classification goals
Types of Traffic Classification
  Port-based approaches
    E.g., TCP port 20 and 21  FTP, TCP port 80  HTTP
  Payload-based approaches
    E.g., “0x12BitTorrent protocol”  BitTorrent
  Machine Learning (ML)-based approaches
    Connection-related statistical information-including connection duration, inter-packet arrival time, and packet
 | Accuracy | Strength | Weakness
Port-based | Low | Low computational cost | Low accuracy
Payload-based | High | Most accurate method | High computational cost Exhaustive signature generation
ML-based | High | Can handle encrypted traffic | High computational cost

## Slide 42: Traffic Classification/Identification (2/2)
In the Perspective of Network Layers
Network Layer
IP, ARP, RARP, etc.
Transport Layer
TCP, UDP, ICMP, etc.
Application Layer
HTTP, HTTPS, SMTP, FTP, TELNET, SSH, POP, etc.
Traffic clustering
Bulk transfer, small transaction, etc.
Application-type breakdown
Web, game, P2P, messenger, streaming, mail, etc.
Application protocol breakdown
HTTP, HTTPS, SMTP, FTP, TELNET, SSH, POP, etc.
Application Breakdown
BitTorrent, MSN, NateOn, Filezilla FTP, etc.
Classification Level in Practice (Classification Output)

## Slide 43: Resource Allocation: Buffering, Scheduling, Shaping, and Marking

## Slide 44: Buffering
Drop-tail FIFO queue
  Packets served in the order they arrive
  … and dropped if queue is full
Random Early Detection (RED)
  When the buffer is nearly full
  … drop or mark some packets to signal congestion
Multiple classes of traffic
  Separate FIFO queue for each flow or traffic class
  … with a link scheduler to arbitrate between them

## Slide 45: Link Scheduling
Strict priority
  Assign an explicit rank to the queues
  … and serve the highest-priority backlogged queue
Weighted fair scheduling
  Interleave packets from different queues
  …in proportion to weights
50% red, 25% blue, 25% green

## Slide 46: Traffic Shaping
Force traffic to conform with a profile
  To avoid congesting downstream resources
  To enforce a contract with the customer
Leaky-bucket shaping
  Can send at rate r and intermittently burst
  Parameters: token rate r and bucket depth d
Tokens arrive (rate r)
Max # of tokens
(d tokens)
packets
tokens
A leaky-bucket shaper for each flow or traffic class

## Slide 47: Traffic Classification and Marking
Mark a packet to influence handling downstream
  Early Congestion Notification (ECN) flag
  Type-of-Service (ToS) bits
Ways to set the ToS bits
  End host sets the bits based on the application
    But, then the network must trust (or bill!) the end host
  Network sets the bits based on traffic classes
    But, then the network needs to know how to classify packets
Identifying traffic classes
  Packet classification based on the “five tuple”
  Rate limits, with separate mark for “out of profile” traffic

## Slide 48: Generalizing the Data Plane

## Slide 49: Data Plane Functions Summary
Basic functional steps:
  parsing, classification, modification, deparsing, and forwarding.
Additional services, such as
  scheduling, filtering, metering, or traffic shaping.
实现方式
  通常都是专用的设备

## Slide 50: 传统网络设备
Traditional networking devices such as routers and switches process packets using data and control plane algorithms.
However, conventional network equipment the data plane functionality is deeply ingrained into the device hardware and software, and hence generally cannot be changed during the lifetime of the device.
Users can configure control plane features and protocols, e.g., via CLIs, web interfaces, or management APIs, but the underlying algorithms can be changed only by the vendor.

## Slide 51: Data Plane Tension
Mordern networks are deployed in different environments, support a variety of use cases, and are subject to requirements ranging from best effort to guaranteed performance.
This wide-spread use and heterogeneity complicate the design of network systems and their main building blocks (devices).
Tension
  Specialization: allows network devices to be optimized for a particular task
  Generality: make network devices commodity and general to reduce engineering cost.

## Slide 52: 传统网络设备
Network Equipment Vendor
Network Owner
ASIC
Team
Software
Team
Feature
Weeks
Years
Years
Feature
Feature
Equipment vendor can’t just send you a software upgrade
New forwarding features take years to develop
By then, you’ve figured out a kludge to work around it
Your network gets more complicated

## Slide 53: Need for Programmability
These opposite forces ultimately pushed the need (and definition) of programmable networking equipment, allowing operators to change device functionality using a programming interface.
Programmability introduces a significant change in the relationship between device vendors and network operators.

## Slide 54: 为什么要实现可编程性
用户角度：A programmable device frees the operator from waiting for the traditional networking equipment’s years-long release cycles
  new feature can be quickly implemented and rolled out directly by the operator using programming interface
设备商角度：Programmability also frees device vendors from designing equipment for a wide range of customer use cases;
  instead, they can invest engineering efforts into optimizing a set of well-defined building blocks that can be used to implement custom logic.

## Slide 55: 现有设备种类众多，但有相似性
Router
  Forward on destination IP address
  Access control on the “five tuple”
  Link scheduling and marking
  Monitoring traffic
  Deep packet inspection
Switch
  Forward on destination MAC address
Firewall
  Access control on “five tuple” (and more)
NAT
  Mapping addresses and port numbers
Shaper
  Classify packets
  Shape or schedule
Packet sniffer
  Monitoring traffic

## Slide 56: 抽象
网络技术发展离不开抽象
  IP是对多种底层连接技术的抽象
  TCP是对端到端可靠性的抽象
多种数据平面设备都被抽象为统一的match-action设备
  匹配：包头对应字段
  操作：实现对数据包的丢包、修改、缓存等操作

## Slide 57: 用match-action抽象来统一各种设备
Router
  Match: longest destination IP prefix
  Action: forward out a link
Switch
  Match: destination MAC address
  Action: forward or flood
Firewall
  Match: IP addresses and TCP/UDP port numbers
  Action: permit or deny
NAT
  Match: IP address and port
  Action: rewrite address and port

## Slide 58: OpenFlow
数据平面提供match-action
Match
  Match on a subset of bits in the packet header
  E.g., key header fields (addresses, port numbers, etc.)
  Well-suited to capitalize on TCAM hardware
Action
  Perform a simple action on the matching packet
  E.g., forward, flood, drop, rewrite, count, etc.
控制平面集中控制数据平面 Controller
  Software that installs rules and reads counts
  ... and handles packets the switch cannot handle

## Slide 59: Match-Action Abstraction
OpenFlow has become quite well-known as an interface between the control plane and the forwarding plane
“Match-Action” is the key:
  Roughly, a subset of packet bytes are matched against a table; the matched entry specifies a corresponding action(s) that are applied to the packet.
Priority | Predicate | Action
5 | dst_ip = H1 | Fwd 1
5 | dst_ip = H2 | Fwd 2

## Slide 60: Data-Plane: Simple Packet Handling
Simple packet-handling rules
  Pattern: match packet header bits
  Actions: drop, forward, modify, send to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
src=1.2.*.*, dest=3.4.5.*  drop
src = *.*.*.*, dest=3.4.*.*  forward(2)
3. src=10.1.2.3, dest=*.*.*.*  send to controller

## Slide 61: Control/Data Separation
SDN makes network devices programmable by introducing an API that allows users to bypass the built-in control plane algorithms and to replace them with self-defined algorithms.
Those algorithms are expressed in software and typically run on an SDN controller with an overall view of the network.
Thereby, complex control plane algorithms designed for distributed control can be replaced by simpler algorithms designed for centralized control.

## Slide 62: SDN可编程
Move control plane out of the switch onto a server.
Well-defined API to data plane (OpenFlow)
  Match on fixed headers, carry out fixed actions.
  Which headers: Lowest common denominator (TCP, UDP, IP, etc.)
Write your own control program.
  Traffic Engineering
  Access Control Policies
Thus, SDN makes control plane programmable.
Notes: Remind them that OpenFlow is based on match + action.
But it is restricted to a specific set of headers, and nothing more.

## Slide 63: Data Plane Programmability
With SDN, Device functionality has become much more flexible and dynamic.
However, OpenFlow is not enough
  allow packet processing on a fixed set of fields only
OpenFlow assumed a specific data plane functionality
  It executed the sole, although relatively flexible, algorithm defined by the OF specifications.
  fixed function data plane can not be changed.

## Slide 64: OpenFlow不能真正软件定义
OpenFlow最早将数据平面的转发逻辑和控制平面的控制逻辑解耦 合，OpenFlow 协议中事先定义协议字段，控制平面按照已有的协议对数据平面进行控制。如果需要增加新的功能就需要对 Openflow 协议进行扩展。
因此 OpenFlow本质上是协议相关的，并非真正的完全“软件定义”
但是，在固定功能数据平面仍然在广泛应用的情况下，OpenFlow 为向 SDN 的平滑过渡提供了支持

## Slide 65: The solution: a programmable switch
data plane programmability means that the data plane with its algorithms can be defined by the users
Change switch however you like.
Each user ”programs” their own algorithm.
Much like we program desktops, smartphones, etc.
Notes: Pause for question: Why might you ever want to change your network’s switches?

## Slide 66: Programmable data planes
Programmable data planes enable users to implement their own data plane algorithms on forwarding devices.
Users, e.g., programmers, practitioners, or operators, may define new protocol headers and forwarding behavior, which is without programmable data planes only possible for a vendor.

## Slide 67: 可编程数据平面
完全可编程的数据平面通常是协议无关的，提供了更加灵活的功能

## Slide 68: Is Software Router Possible?
Of course, we can implement Match-Action in software on a general purpose CPU.
But for the speeds we are interested in dedicated hardware.

## Slide 69: Early attempts at programmable routers
Chart: Performance scaling
| 1999 | 2000 | 2002 | 2004 | 2007 | 2009 | 2010 | 2014
Software router | 0.1 | 0.17 | 4 | 35 | 40 | 100
Line-Rate router | 32 | 80 | 240 | 640 | 3200
10—100 x loss in performance relative to line-rate, fixed-function routers
Unpredictable performance (e.g., cache contention)
Notes: How would _you_ design a programmable router?
Mention that it is on log scale
Define line rate
Unpredictable performance examples: hardware config (number of cores, RAM size, etc.)

## Slide 70: The RMT model: programmability + performance
Reconfigurable match tables, such as RMT , allow the programmer to match on and modify all header fields (or arbitrary bit ranges) making the devices significantly more flexible and capable.
Performance: 640 Gbit/s (also called line rate), now 6.4 Tbit/s.
Programmability: New headers, new modifications to packet headers, flexibly size lookup tables, (limited) state modification
Notes: What is match-action?
Why use a pipeline?

## Slide 71: RMT: Two simple ideas
Programmable parser
Pipeline of match-action tables
  Match on any parsed field
  Actions combine packet-editing operations (pkt.f1 = pkt.f2 op pkt.f3) in parallel
Notes: This is all you really need to know about the paper 
The rest is just how to make it run at 1 GHz
The idea that you can take different logical tables and split them across pipelines in a flexible way.

## Slide 72: Programmable parser (Gibb et al. ANCS 2013)
State machine + field extraction in each state (Ethernet, IP, etc.)
State machine implemented as a TCAM
Configure TCAM based on parse graph
Notes: Say that it’s not very different from how grep works on Linux.

## Slide 73: Match/Action Forwarding Model
Programmable Parser
Deparser
In
Queues
Action
Stage 1
Match Table
Action
Stage 2
Match Table
…
Data
Out
Action
Stage N
Match Table
Match
Action Stage
Match
Action Stage
Match
Action Stage

## Slide 74: 协议无关的交换机架构 PISA
包括可编程的解析器（parser），可重构的流水线（pipeline）和可编程的逆解析器（deparser）三个部分

## Slide 75
解析器可以看做是一个有限状态机，将报文头字段按照预先定义的格式和方法层层解封装。解析器是可以编程的，以支持用户自定义的数据包头格式，实现对新网络协议的支持。
流水线由多个流水级组成，每个流水级包含多个可编程的处理单元，可以并行对报文执行操作。
逆解析器重新将报文封装，将修改后的报文头字写回报文。

## Slide 76: Benefits
Data plane programming introduces full flexibility to network packet processing,
  i.e., algorithms, protocols, features can be added, modified, or removed by the user.
In addition, programmable data planes can be equipped with a user-defined API for control plane programmability and SDN.
  To keep complexity low, only components needed for a particular use case might be included in the code. This improves security and efficiency compared to multi-purpose appliances.

## Slide 77
User: Allows network equipment designers and even users to experiment with new protocols and design unique applications;
  both do no longer depend on vendors of specialized packet-processing ASICs to implement custom algorithms.
Vendor: beneficial for network equipment developers that can easily create differentiated products despite using the same packet processing ASIC.

## Slide 78: Programming RMT: P4
RMT provides flexibility, but programming it is akin to x86 assembly
Concurrently, other programmable chips being developed: Intel FlexPipe, Cavium Xpliant, CORSA, …
Portable language to program these chips

## Slide 79: P4
P4 作为一种交换机配置的高级语言，它具有三个特性：
（1）可重构性：也就是可以重新配置部署，当交换机被设定好之后，网络开 发人员也可以根据自身需要更改交换机处理数据流的方式，实现定制“现场”的 可重构能力。
（2）协议无关性：交换机的可编程不需要与任何特定的厂商绑定各种网络协 议，而是通过自定义解析流程，设定匹配顺序和编写数据流控制程序实现数据分 组的转发。
（3）目标无关性：开发人员不需要关心底层特定硬件设备的具体实现细节就 可完成对数据包处理过程进行编程的操作，而与交换机事先设置程序设定的目标 无关。

## Slide 80: P4 main ideas
Abstractions for
  Programmable parser: headers, parsers
  Match-action: tables, actions
  Chaining match-action tables: control flow
Notes: Emphasize that this is a first step and things will get better.

## Slide 81: Domain Specific Processors
CPU
Computers
Java
Compiler
GPU
Graphics
OpenCL
Compiler
DSP
Signal
Processing
Matlab
Compiler
Machine
Learning
?
TPU
TensorFlow
Compiler
PISA
Networking
P4
Compiler
>>>

## Slide 82
Match+Action Stage
Memory
ALU
Programmable Parser
Programmable Match-Action Pipeline
PISA: Protocol Independent Switch Architecture

## Slide 83
PISA: Protocol Independent Switch Architecture

## Slide 84
Memory
ALU
Programmable Parser
Programmable Match-Action Pipeline
header_type ethernet_t { … }
header_type l2_metadata_t { … }
header ethernet_t ethernet;
header vlan_tag_t vlan_tag[2];
metadata l2_metadata_t l2_meta;
Header and Data Declarations
Parser Program
parser parse_ethernet { extract(ethernet); return switch(ethernet.ethertype) { 0x8100 : parse_vlan_tag; 0x0800 : parse_ipv4; 0x8847 : parse_mpls; default: ingress; }
Tables and Control Flow
table port_table { … }
control ingress { apply(port_table); if (l2_meta.vlan_tags == 0) { process_assign_vlan();
} }
Example P4 Program

## Slide 85: P4 Scope
Control plane
Data plane
Control traffic
Packets
Table mgmt.
Traditional switch
Control plane
Data plane
P4 Program
P4-defined switch
P4 table mgmt.
Notes: This is the P4 API: a new API between the control-plane and the data plane.
The data plane performs mostly stateless high-speed processing.
The data plane is lean and fast; most of the complexity is still in the control plane. P4 does not address this aspect.

## Slide 86: Q: Which data plane? A: Any data plane!
Control plane
Data plane
Programmable switches
FPGA switches
Programmable NICs
Software switches
Notes: P4 should be portable across a large spectrum of switch implementations.

## Slide 87: Reflections on a programmable switch
Why care about programmability?
  If you knew exactly what your switch had to do, you would build it.
  But, the only constant is change.
  (Hopefully) no more lengthy standard meetings for a new protocol.
  Move beyond thinking about features to instructions.
  Eliminate hardware bugs, everything is now software/firmware.

## Slide 88: Thank You.
Slides courtesy of
Patrick Bosshart, Nick McKeown, and Mihai Budiu, P4 Tutorial
Yashar Ganjali, CSC 2229 Course
Jennifer Rexford, COS 561 Course
James Won-Ki Hong, SDN course